## Slide 1: Graphics Display Devices
Lecture 2

## Slide 2: Vector Displays
  Early computer displays: basically an oscilloscope
  Control X,Y with vertical/horizontal plate voltage
  Intensity or brightness of the display is sometimes called the Z axis.
  Vector Drawing Commands are mentioned below
Notes: An oscilloscope is a laboratory instrument commonly used to display and analyze thewaveform of electronic signals.
In effect, the device draws a graph of the instantaneous signal voltage as a function of time.
Oscilloscope is electronic test equipment that allows to signal voltages to be viewed usually as a 2D graph.

## Slide 3: Vector Displays
Each line segment to be displayed takes very few data values
  Vector displays can draw a picture very rapidly
  Each XY pair is used to generate deflection voltages
    which will sweep the beam across the face of screen
  When the beam strike the phosphor,
    visible light is produced for certain time
Notes: Deflection voltages i.e bend voltages,, that are reflected

## Slide 4: Vector Displays Disadvantages
Complex object drawing is difficult
  list of commands becomes very long
Complex scenes
  visible flicker
  first line may have faded out before last is drawn
Vector displays can not show
  smoothly shaded regions
  Scanned images
  Cross hatching effect
Notes: Flicker: light that vary rapidly in brightness

## Slide 5: Display Technologies
Cathode Ray Tubes (CRTs)
  Most common display device today
  Evacuated glass bottle
  Electrons pulled towards anode focusing cylinder
  Vertical and horizontal deflection plates
  Beam strikes phosphor coating on front of tube

## Slide 6
Notes: a perforated metal sheet that ensures that the electron beam hits only the correctly colored phosphor dots and does not illuminate more than one dot.
. The shadow mask absorbs electrons that are directed at the wrong color phosphor.

## Slide 7
Phosphers
  Flourescence:
    Light emitted while the phospher is being struck by electrons
  Phospherescence:
    Light emitted once the electron beam is removed
    emits visible light for a certain period after the bombardment has ceased
  Persistence:
    Time from the removal of the excitation to the moment when phosphorescence has decayed to 10% of the initial light output
    Long persistence -> image smears as picture is moved on screen.
    Short persistence -> no smearing as image moves but more refreshing needed
Notes: Mark , dirty , damage
persistence is the time to which the phosphors in the CRT emit light until the next electrons is fired.

## Slide 8: CRT Display Devices
Monitors
Plotters
Data Matrix
Laser printers
Video digitizer
Scanners
LCD Panels
Keyboard
Mouse,
A few examples of Computer Graphics devices are:

## Slide 9: CRT
CRT monitor is most commonly used device
Types of CRT monitors:
  1. DVST(Direct View Storage Tube)
  2. Calligraphic or Random scan Display system
  3. Refresh and Raster Scan Display System.
  The common feature in all these three display devices is the cathode ray tube.

## Slide 10: DVST
Long persistent Phosphor.
Doesn’t need to refresh
Provides flicker free display
A slow moving electron stream draws a line on the screen.
The screen has a storage mesh in which the phosphor is embedded.
Image is stored as a distribution of charges on the inside surface of the screen.
It has very limited interactive support.

## Slide 12: Calligraphic or Random Scanned Display Systems
Vector stroke or line drawing display because the electron beam is deflected from one point to another
Those sequence of commands that guide the beam to move from one point to another in order to create short strokes or lines

## Slide 13
  Raster Displays
  Raster: A rectangular array of points or dots
  Pixel: One dot or picture element of the raster
  Scan line: A row of pixels

## Slide 14: Raster Displays Contd…
Video Monitor
Flat panel
Laser printer
Dot matrix
Ink jet plotter
Film recorder

## Slide 15: Raster Displays Contd…
Line/vector display raster display
no pixels array of pixels

## Slide 16: Raster displays
  Fixed scan pattern
    left to right, top to bottom
  To paint the screen, computer needs to synchronize with the scanning pattern
    Framebuffer
      special memory to buffer image with scan-out synchronous to the raster display device.
      Region of memory should be large enough to hold all pixel values
  Graphic card
      House the memory require for frame buffer
Notes: Graphic card: The graphics components that control and enhance how graphics (pictures, videos, programs, animation, 3D) are displayed on your screen.
Frame buffer:
Contains color value of every pixel.
large, contiguous piece of computer memory.

## Slide 17: Scanning process
RGB Frame buffer
Notes: Dac is used to produce primary colors, which converts digital or logic values 01 into voltages.

## Slide 18: Index Colour and lookup table
Each pixel go through an intermediate step
  Before they drive CRT
These bits are used as an index in to a table of 2n values

## Slide 19: Color is expensive …
The more color you want, the more bits you will need for each pixel
Exercise: 1024 x 1280 screen with
24 bits per pixel, how large is the frame buffer?
1024 x 1280 x 24 / 8 = 4M Byte
Notes: 1 MB = 1024 KB
(X-Resolution * Y-Resolution * Bits-Per-Pixel) / (8 * 1,048,576)
640 × 480 × 12 bits ÷ 8 bits per byte = 450 B in order to convert into KB, divide the result by 1024 1280 × 1024 × 12 bits ÷ 8 bits per byte = 1920 B 2560 × 2048 × 12 bits ÷ 8 bits per byte = 7680 B For 24 bits of storage per pixel, each of the above values is doubled.

## Slide 20
Efficient Mapping: LUTs efficiently map input values to output values, facilitating tasks like color correction and grading.
Color Correction and Grading: They are commonly used for color correction and grading to achieve desired looks or correct color inaccuracies.
Real-time Rendering: In real-time graphics, LUTs help achieve effects like color grading without significant computational overhead.
Non-linear Effects: LUTs are useful for applying non-linear effects such as gamma correction or tone mapping efficiently.
HDR Imaging: They play a role in HDR imaging by implementing tone mapping operators effectively for displaying high dynamic range images on standard displays.

## Slide 21: LUT
It maps input values to output values for fast processing
It stores precomputed values
Quick retrieval and improve efficiency
Used In Digital signal processing (IP , graphic rendering)
Computer Graphics (texture shading mapping)
Mathematical computation( log values, exponential functions)
Machine Learning , AI. Descision making, fast interference

## Slide 22: Colour Index Framebuffer

## Slide 23
24 bits per pixel
8 bits per pixel
Without lookup table
With lookup table
Frame buffer memory = 4MB
Frame buffer memory = 1 MB

## Slide 24: Color Lookup Table
only 3 bits per pixel
But one insist on having high quality pictures …
Use Color Look Up Table (LUT)
3 bits/pixel frame buffer
R G B
You can still have 24 bits
in each of the color table
entries
0
1
2
3
4
5
6
7
24 bit wide

## Slide 25: LUT memory
If Raster display has color depth= b bits
Each LUT entry is w bits wide then
System can display
  2w colors 2b at one time
So it require very little memory
  Only 2b words of w bits each
  System have capability of 24 bit colors
  Frame Buffer
    1024 x 1280 x 8 / 8 = 1M Byte
  LUT
    768 bytes (2b *w/8 )
Notes: B never exceeds w.
B=8
w=24
(2^8 * 24)/8

## Slide 26
Summarizing LUT
    System has color depth of b bits.
    LUT entry is w bit wide
    System will display: 2w colors 2b at one time
  Relationship b/w bitplanes and width of LUT
    W is multiple of 3 derive each DAC.
  Memory required by LUT
    2b *w/8
  Storage required by System
    b/3*rows *cols + size of LUT
Notes: 3 bits will have 8 values

## Slide 27
  Size of frame buffer:
      rows *col * bits per pixel/ 8
  size of LUT
      2b *w/8
  Storage required by System
      b/3*rows *cols + size of LUT
Notes: 3 bits will have 8 values

## Slide 28: Task 1
A system with b=8 bits and LUT width w=12 can display _____________ colors , and ___________ colors at 1 time?
A system with b=8 bits and LUT width w=24 can display ____________ colors , and ___________ colors at 1 time?
A system with b=12 bits and LUT width w=18 can display _____________ colors , and ___________ colors at 1 time?
Notes: Solution 1: 4096 total and 256 1 time
Solution 2: 16777,216 total and 256 1 time
Solution 3: 256 K 262144 colors and 4096 at a time.

## Slide 29
Exercise:
640 × 480 screen with 12 bits per pixel, how large is the frame buffer?
1280 x 1024 screen with 12 bits per pixel, how large is the frame buffer?
2560 × 2048 screen with 12 bits per pixel, how large is the frame buffer?

## Slide 30
1 MB = 1024 KB
(X-Resolution * Y-Resolution * Bits-Per-Pixel) / (8 * 1,048,576)
640 × 480 × 12 bits ÷ 8 bits per byte = 450 B in order to convert into KB, divide the result by 1024
1280 × 1024 × 12 bits ÷ 8 bits per byte = 1920 B
2560 × 2048 × 12 bits ÷ 8 bits per byte = 7680 B

## Slide 31: Display Technology: LCDs
Liquid Crystal Displays (LCDs)
  organic molecules
    naturally in crystalline state
    that liquefy when excited by heat or E field
  Crystalline state twists polarized light 90º.
Notes: It converts electric field into visible dots on the screen .
Electric field causes the polarization of crystals.
LCD is composed of several layers which include two polarized panel filters and electrodes. Light is projected from a lens on a layer of liquid crystal. (formed as electric current flows through the crystal) forms the colored image. This image is then displayed on the screen.
to cause light waves to vibrate in a particular pattern
TN: twist and untwist at varying degrees to allow light to pass through

## Slide 32: Display Technology: LCDs
Converts electric field to visible dots
Each pixel is addressed by horizontal and vertical grid wire
Notes: Each pixel is displayed on the fixed grid or on the fixed predefined sequence. Frame
Predefined frame or mold on which each point will be displayed.

## Slide 33: Active matrix panels
Are LCD panels
Have tiny transistors at each pixel
Transistors responds to electric field
  adjusts the liquid crystal by an amount proportional to the field
  Allow the display of different level of brightness
Transistors provide some “memory”
  that holds the crystals in their adjusted states
  so that the display need not be refreshed
This produce much brighter display
Notes: Tiny transistor is present on each pixel location . transistor have some memory that will allow to save the crystal state. So display needed not to be refreshed.

## Slide 34: Display Technology
Plasma
  Display geometry
  Neon bulb turn on and off by electric field
DMD / DLP
  optical semiconductor, called a Digital Micromirror Device (DMD),
  uses mirrors made of aluminum to reflect light to make the picture
Organic LED Arrays
  It consists of a series of organic layers between two electrical contacts (electrodes).
  Each layer is deposited on the other, creating a single unit.
Notes: Geometry means vertical grid and horizontal grid. So the plasma need not to be refreshed.
DMD; : resolution , brightness, contrast.
LED : light emitting diode (elecrodes)

## Slide 35: Hard Copy Raster Devices
Film Recorder
  Strip of photographic film
  electron beam exposes as it sweeps over it in raster pattern
  Electronic Hard copy of Image
Laser Printer
  Sweep a laser beam on internal defined buffer
  Surface becomes electronically charged causing toner to follow spots.
Notes: Hard copy raster devices are used when you want the permanent version of the image usually on the paper. Devices draw the pictures by transferring the information from the buffer to the display medium.
Toner is then transferred into the paper, to create the image,
  Film recorder Have their own frame buffer or camera mounted on CRT

## Slide 36
InkJet Plotter
  A tiny nozzle sweeps over the paper and squirts (sprays) proper color of ink at each pixel position.
Post Script Language
  Printer are equipped with micro processor.
  Generate high quality text and graphics
Notes: Post script language can generate the high quality text and graphics on the printed page.